## Slide 1: Optimizing Pulse Shape Discrimination in a PEN Scintillator
Eli Ward

## Slide 2: Scintillation Overview
Radiation ejects electrons or protons from molecules in scintillator
Ejected charged particles ionize nearby atoms
  When ionized atoms recaptured electrons, they are in excited state
Excited states in molecules decay to lower energy states and produce scintillation (characteristic pulses of photons)
Radiation includes gamma rays, neutrons, muons, alpha particles
  Gamma rays eject electrons, neutrons produce nuclear recoils
  Muons and alpha particles ionize atoms directly
Notes: Nuclear recoil out of atom
Electrons and muons are low ionizing particles, travel very far but produce different levels of ionization than ions
Protons are highly ionizing particles, travel much shorter distances with same initial energy
Recaptured electrons in excited states can immediately decay to ground states if they have opposite spin as the ground state
If recaptured electrons in excited states have same spin as the ground state, they form a triplet state and that is a first forbidden decay

## Slide 3: Delayed Fluorescence vs Phosphorescence
Recoiling electrons fluoresce mainly via decaying singlet states
  Singlet states decay quickly
Recoiling protons fluoresce via decaying singlet states and triplet-triplet annihilation
  Triplet-triplet annihilation results in delayed fluorescence
Can see that scintillation pulse from proton has longer tail
Notes: Electrons move quickly, don’t spend very much time near atoms, so don’t create many (more complex) triplet states
Protons with same energy move much more slowly, spend more time near atoms, create greater density of triplet states
Single triplet states will phosphoresce
Arrow is intersystem crossing (no intersystem crossings in PEN)
Dashed lines are vibronic energy levels, solid lines are electron energy levels
Protons at the end of their recoil capture electron and become hydrogen
Electrons at the end of their recoil get captured by atom

## Slide 4: What makes a good scintillator?
Efficient conversion of ionization to light
  10,000 photons/MeV
Transparent to light created within scintillator
  Attenuation length of ~1 m
Produces easily detectable wavelengths of light
  UV to visible light
PEN scintillators:
  Produce ~3500 photons/MeV
  Have attenuation length on the order of centimeters
  Have peak scintillation at ~450 nm
Notes: Don’t want light to be absorbed by scintillator and converted to heat
Good scintillators produce ~10,000 photons/MeV (energy of electronic recoil, nuclear can have quenching)
PEN produces 3500 photons/MeV
Quenching = Amount of light lost
Good scintillators have an attenuation length of ~1 m
PEN scintillator has attenuation length on the order of centimeters
Attenuation length describes distance traveled through scintillator it takes for probability of photon being absorbed to reach 1/e = 63%

## Slide 5: Advantages of PEN Scintillators
Polyethylene naphthalate (PEN) is a pretty good but not great scintillator material, so why are we interested in it?
High yield strength at cryogenic temperatures
  Useful in experiments with germanium detectors (77 K)
Chemically resistant, can be aggressively cleaned with acids
  Minimizes radiation contamination for use in low background measurements
Notes: Polymer; chain of carbon, hydrogen and some oxygen atoms
450 nm, easy wavelength range to detect with PMTs
low background (few number of events)

## Slide 6: Pulse Shape Discrimination
PSD: Ratio of area under pulse tail to area of entire pulse
FOM (Figure of Merit): Describes how easily electron and proton scintillation pulses are distinguished
Notes: Long gate vs short gate?
  Proton has longer pulse tail, electron has shorter pulse tail (b/c singlet states)
  Pick point where you can distinguish between proton tail and electron tail
Mu_e/p = average e/p PSD value
W_e/p = Width of pulses
Want to decrease W values and increase separation between pulses, but that is very hard with this PSD method
Gate = cutoff

## Slide 7: Gamma Ray and Neutron Sources
7Li(p, n)7Be and 13C(α, n)16O emit neutrons in all directions, but with characteristic energies at each angle
  PMT can swivel around reaction point to capture specific neutron energies
Gamma rays come from background interactions and 13C(α, n)16O
  Background interactions include beta decay of potassium-40, releases gamma ray at 1.5 MeV
  13C(α, n)16O emits gamma rays at 6 MeV
Notes: The objective of this measurement is an R&D effort in the LEGEND experiment to characterize PEN
7Li(p, n)7Be = Lithium target, proton hits target, neutron flies out, Beryllium left over
Incident particle hits target, creates neutrons flying in every direction, but neutrons have specific energies at specific angles, move scintillator around to specific angles to capture specific neutron energies
Gamma rays come from background interactions and 13C(alpha, n)16O also emits gamma rays at 6 MeV
Background interactions example: potassium-40 is naturally occurring everywhere, beta decays and releases a gamma ray when it does at 1.46 MeV
https://chem.libretexts.org/Bookshelves/Physical_and_Theoretical_Chemistry_Textbook_Maps/Supplemental_Modules_(Physical_and_Theoretical_Chemistry)/Spectroscopy/Electronic_Spectroscopy/Jablonski_diagram
Silver tube is vacuum tube carrying H++ and He++ beam, Li or C foil on tantalum backing at end of tube, water cooled, PMT on a table can swivel around

## Slide 8: Sample of Data Used
Bin width is 4 ns
Energy deposition is in range of E = 1 – 4.5 MeV
Low energy measurements cut out
Gamma Trace
Neutron Trace
Notes: Shape of scintillation pulse called waveform or trace
Each bin is one sample taken in 4 ns (width of each bin is 4 ns)
Higher energy deposition creates larger signal, higher amplitude
Energy deposited by gamma rays and neutrons into scintillator (a little more complicated, but this is good enough)
  E = 1 – 4.5 MeV

## Slide 9: Machine Learning Basics
Neural networks take in some inputs D = {xn} Nn=1
Perceptron NN feeds forward with linear activation function
  alj = zlj = Σk wljk*al-1jk + blj
More advanced NN use nonlinear activation functions
  E.g., sigmoid function alj = σ(zlj)
    σ(z) =
Neuron only “fires” if alj is above some threshold
  Threshold for perceptron neuron is zero
Get out some output function f(x)
Output function f(x)
x1
x2
x3
x4
Input Layer
Hidden Layer
Output Layer
w11
b11
b12
w12
a01
a02
a03
a04
a11
a12
a31
Inputs
Notes: Perceptron neurons fire if z is above some threshold; if neuron doesn’t fire, it just doesn’t propagate forward
Another activation function (that I don’t have time to discuss) is the “relu” function

## Slide 10: Backpropagation
After getting output from NN, can calculate the cost function to understand how accurate output is
Simplest cost function C(w) is mean squared error
Minimize C(w) to maximize NN accuracy
Backpropagation algorithm computes error for output layer, then propagates that error back to previous layers, recalculating weights and biases as it does so
Then run NN again with new weights and biases and calculate C(w) again
Notes: y is target – “correct answer”
)
y is target – “correct answer”
Δ_𝑗^𝐿=𝜕𝐶/(𝜕𝑧_𝑗^𝐿 )=(𝑎_𝑗^𝐿−𝑦_𝑗)𝑓^′ (𝑧_𝑗^𝐿)

## Slide 11: Binary Classification
NN maps some input data to a set of binary classes
   Є {0, 1}
Two sets of inputs: Data and Labels
Cost function is binary cross entropy

## Slide 12: Specific Classification Project
Inputs:
  Randomly ordered list of 10,000 gamma pulses and 10,000 neutron pulses
  Second list of 1’s and 0’s labeling events in first list
Architecture:
  Input layer: Dense, 10 neurons, input shape = 200, ReLU activation function
  Hidden layer: Dense, 5 neurons, ReLU activation function
  Output layer: Dense, 1 neuron, sigmoid activation function
Cycles through NN 10 times
Batch Size = 1,000

## Slide 13: References
Thank you to Yuri Efremenko, Brennan Hackett and Jesse Harris
B. Hackett, R. Toomey, “Measurement of Luminescent Properties of Polyethylene 2,6-Naphthalate,” (2021).
Hackett, Brennan. Scintillation and Optical Properties of the Low-Background Scintillator, PEN. 2021. PowerPoint Presentation.
J. Harris, “An A.I. Approach to Higgs Decay,” (2020).